## Slide 1: O3 System Sales Presentation

## Slide 2: O3 System - Benefits

## Slide 3
Market Convergence
CONVERGENCE
Tech, industry & markets are converging.

## Slide 4
VISION OF INTEGRATED ROOM CONTROL
VISION
Integrated Room Control increases a building’s value…
Higher Productivity
Increased Value
Optimized Occupant Experience
EarthrightTM Energy Efficiency
Reduced Operating Costs

## Slide 5
A single edge controller brings all disciplines together and so a room behaves as a room – not a collection of unrelated data points passed to an upper level.
Integrate means the lighting controller, the HVAC controller and the access controller are tied together at some central point in the building.
Converge all controls in a single controller that knows what a “room” is.
Convergence versus Integration

## Slide 6
?
I/O
I/O
Lighting
Air Quality
Occupancy
Temperature
Chilled Beam
Humidity
Ventilation
Shades
Window Contacts
Heating

## Slide 7
Bringing the protocols together in the room
P E

## Slide 8
enteliWEB

## Slide 9
MEETING ROOM
Activity Meeting Mode
Set Point 21°C
CO2 Level 1300ppm
Top Lighting 60%
Shades Auto
Music Level 40 dB
Sound Level 65dB
# People 9
TV Mode 1

## Slide 10: O3 System
O3-DIN Flexible I/O
O3-HUB
  Rich Sensors
  Wireless
O3 Room Control App
enteliWEB
enteliWEB
Notes: When we talk about the O3 it isn’t just the Hub, and it’s not just the DIN modules – it’s the overall system and that includes the App, the eWEB services API and all the features we’ll talk about here.

## Slide 11: O3 System - Components
Controllers and Modules

## Slide 12
Integrated Room Control
FLEXIBLE. MODULAR.
CPU Protocol integration
HVAC (Heating, Ventilation, Cooling)
Lighting Control (DALI, I/O)
Shades Control (I/O, SMI)
Access control
Improved Occupant Experience with visual and audio feedback
Local Analytics
Integrates everything in a room with protocol modules and a sensor hub

## Slide 13
DIN-SRC
Up to 32 I/O
Product Position
Notes: When promoting to partners, …
DSC and eBUS have a cost per I/O
eBUS has its own features that differentiate – dense I/O, HAO switches, Hot swapping
O3-DIN with 8xP modules has a lower cost per I/O point than the DSC and eBUS.
It doesn’t compete directly with DAC’s. They are still the lowest cost

## Slide 14
2 x RS 485
2 x RJ45
Ethernet
BACnet/IP
2 x
USB
8 x UI/UO
AI, BI, AO,
LO, BO, MI
1 x RS485
BACnet
MS/TP
Shades
Space-saving design
for DIN rail mount in
Electrical sub-panels

## Slide 15: Integration Engine: CPU
Specification
  600 MHz
  4GB eMMC Flash Storage (2 GHz)
  256 MB DDR3L RAM
  Ultracap Backup for RTC and CPU Data
Power
  24 VDC Input
  3 x 24 VDC Output to supply
    Thermostats
    3rd Party Devices
    Power Injectors
    Hubs
    Etc.

## Slide 16: Single Room Integration Engine: SRC
Specification
  600 MHz
  4GB eMMC Flash Storage (2 GHz)
  256 MB DDR3L RAM
  Ultracap Backup for RTC and CPU Data
Power
  24 VDC Input
  1 x 24 VDC Output to supply
    Thermostats
    3rd Party Devices
    Hubs
    Etc.

## Slide 17: Integration Engine CPU
Communications
  2 x Ethernet (10/100MB)
    BACnet IP, BACnet over Ethernet
    Daisy Chain capable
  3 RS-485
    NET1 – MS/TP, LINKnet, Modbus, etc.
    NET2 – MS/TP, LINKnet, Modbus, etc.
    NET3 – O3BUS, MS/TP, LINKnet, Gateway
  2 x USB (Host)
    Storage, Upgrades, Wireless, Charging
  Status LED
    Green – Normal
    Yellow – No Fieldbus Power
    Red – Fault, Error
  NET Port LED
  Ethernet LED

## Slide 18: Single Room Integration Engine SRC
Communications
  2 x Ethernet (10/100MB)
    BACnet IP, BACnet over Ethernet
    Daisy Chain capable
  1 RS-485
    NET1 – MS/TP, LINKnet, Modbus, etc.
  1 O3BUS (CAN-based)
    NET3 – Hubs & Power Injectors
  2 x USB (Host)
    Storage, Upgrades, Wireless, Charging
  Status LED
    Green – Normal
    Yellow – No Fieldbus Power
    Red – Fault, Error
  NET Port LED
  Ethernet LED

## Slide 19: Power Supply
24 VDC in
24 VDC out
AND PoE Ready
New 2019 Q1

## Slide 20: Universal I/O: O3-DIN-8xP
  Software configurable: AI, BI, MI, AO, BO, LO
  No Jumpers!
  Any I/O mix of 8 inputs and outputs

## Slide 21: Binary Outputs O3-DIN-4F4xP
Objects
  BO
Characteristics
  4 FET outputs
  500mA output current
  Staus LED
  AC or DC voltage switching
  4 universal I/O pins included
New 2019 Q1

## Slide 22: DALI
Objects
  LC – Lighting Control Object
    Light Group control
    Motion Sensor inputs
  LO – Lighting Output Object
    Define output control (Dimming, Fading, Blink Warn, etc.)
Characteristics
  64 Ballasts
  64 input Devices
    Switches
    Occupancy Sensors
  Staus LED
  DALI 2-wire Network
  Power supply in the two wires
  100mA DALI power supply built-in

## Slide 23: SMI
Characteristics
  16 Shades Motors
  16 Groups
  Staus LED
  SMI LoVo & Line Voltage
  Power supply in the two wires
  Up & Down override buttons for commmissioning
  30mA power supply built-in

## Slide 24: Power Injector
Characteristics
  8 address positions by rotary switch
  1 Power Supply input
  Staus LED & O3BUS LED
  1 O3BUS 3 pin connection
  2 Power Supply outputs
  Built-in O3BUS termination
Benefits
  Connect more modules to controller
  Mount I/O remote from the controller
New 2019 Q1

## Slide 25: Room Applications
Larger Room
HVAC
Light, Blinds
Multiple Rooms
HVAC
Light, Blinds
CPU
PWR INJ

## Slide 26: O3-DIN-ACCESS Module
IO interface for a typical single door / credential reader
IO specific to access control application
  Wiegand input with LED output
    26 bit
    37 bit
    37 bit facility
    Simple 32
  Supervised input circuits - Door Contact and RTE
  Door lock outputs
  12V/24V power output
  Additional Universal IO - Software configurable
Supports multi-format reader from one input interface
Card reader
REX
Power in
Door
lock
Door
contact
Universal
point
New 2019 Q1

## Slide 27
Ethernet
MS/TP
LINKnet
Universal I/O
Inputs: 10k, 0-5VDC, 0-10VDC, 4-20mA
Outputs: 0 to 5 V output, 0-10VDC (Source 20mA, Sink 10mA)
Occupant Comfort, Energy Saving
Temperature, Occupancy, Light, Humidity
Audio signature Occupancy
Bluetooth Location beacon
AV Equipment
Connectivity

## Slide 28: System Wiring O3-DIN-CPU
Up to:
8 Remote Hubs
4 modules directly attached to CPU
4 modules to each Power Injector unit
12 modules per CPU
24 if they are Access Door Modules

## Slide 29: System Wiring O3-DIN-CPU
Up to:
8 Power Injectors
4 modules directly attached to CPU
4 modules to each Power Injector unit
12 modules per CPU
24 if they are Access Door Modules
. . .
e.g. Up to 6 O3-DIN-PWRINJ if 2 hubs connected

## Slide 30: Low Cost: Single Room Controller
Low Cost little brother of O3-DIN-CPU
1 serial port
2 Hubs maximum
Same power
PoE Ready

## Slide 31: Features and CPU SRC comparison
Same hardware,
Same database,
Smaller architecture
Lower Cost per room

## Slide 32: SRC Versus CPU Controller
CPU System Layout
SRC System Layout
Modbus
Or
LINKnet
Or
MS/TP
Analog I/O
Binary I/O
DALI
Access
Light, Temperature,
Sound,
Occupancy
. . .
#1
#2
#3
#32
Light, Temperature,
Sound,
Occupancy
#1
#2
. . .
#1
#2
#3
#32
#1
#2
#6
Modbus
or
LINKnet
or
MS/TP
PWRINJ
PWRINJ

## Slide 33
O3 Access System
Controllers
O3-DIN-CPU and/or O3-DIN-SRC
O3-DIN-ACCESS
O3-DIN-PWRINJ

## Slide 34: O3 System - Components
Sensor Hub

## Slide 35: Features
8 sensors
3 wireless technologies
Speaker
12 full color LEDs in ring
Temperature
Humidity
Light Intensity
Light Color
Occupancy
Microphones
EnOcean radio Tx Rx
Bluetooth LE radio Tx
Infrared remote Tx
Notes: I want to impress on people that this is a fully featured product with so many elements built-in.
The opportunities are endless
We’ll go into detail on a few of these sensors to show you just how much Delta innovates

## Slide 36: Sensor Fusion: Smart Temperature
Compensates for ceiling mount
Calibrate where you are in the room
IR temperature senses FAST!
  Enables optimum start for occupancy
Infrared Temperature
Digital Temperature
Multi-sensor composite
Notes: A competing product has temperature sensing in the ceiling. They don’t recommend driving heating control from that sensor.
Delta went a step further and projects the temperature into the space with new technologies
Calibrate to the desired temperature, at the desired location. The system now controls to that location with accuracy around that temperature
Compared to a stat on the wall that senses the temperature in one location in the room, the Sensor Hub senses in the middle of the room, or at least where the occupant is more likely to be, and senses a wide area of the room rather than a single point.

## Slide 37
Tracks temperature accurately
Notes: In our test facility with 5 precision temperature sensors in the room, you see the yellow band is the range of those reference temperatures.
Once calibrated, the three hubs shown track right down the middle of the room’s temperature over a 24 hour period
The hub is +/-0.5degrees

## Slide 38: Sensor Fusion: Smart Temperature
15 minutes faster than a wall-stat
Save energy on occupancy, and vacancy cycles
Notes: I said that IR temperature sensing is fast. 15 minutes faster than the stat on the wall.
So, the Optimum Start concept that partners already use for beginning of the day to conserve energy is now available for the moment a room becomes occupied
More efficient and timely comfort while saving energy

## Slide 39
Sensor Fusion Occupancy
PIR Occupancy
Sensor Fusion Occupancy
Microphones
Microphones
IR Temperature Spike
Audio Signature
Infrared Temp.
Occupancy
Notes: Note: PIR triggers occupancy, Audio, infrared both latch it.
Fewer false vacancies, and quick off time after real vacancy
Sensitivities can be adjusted to accommodate quieter spaces, or louder spaces
Up to 10’ height for mounting. Up to 22’ diameter

## Slide 40: Features: Light Sensor
Senses brightness for daylight harvesting applications
Senses Light Color RGB or Temperature in Degrees Kelvin
Color for Circadian Rhythm control and sensing
Color for animal care in university labs
Notes: The light sensor is built in there too. Light intensity in Lux or foot-candles can be read by using the correct AIC object.
Color is a big coming thing in lighting, so we have that in there as well. Sense in RGB values or Color Temperature
Fish like different blue tones to the light so universities are approaching us with requests for color control and sensing that color.
Control of lighting color in elderly care and other medical facilities is reported to have good results for productivity, and wellness. The light sensor aids in bidding on these types of jobs.

## Slide 41
LOCATION
TAMPER AVOIDANCE
OPEN OFFICE
CUBICLES
T-BAR vs WALL INSTALLATION
OCCUPANCY
WALL ACNE
RADIO ANTENNA
INDIRECT SUNLIGHT
CLOSER TO OCCUPANT
EASY TO MOVE WALLS / EQUIPMENT
Notes: Like they say in real-estate it’s all about Location, Location, Location
Look at all these…
Sensing in the right place, not at the doorway,
Senses light from the ceiling out of the direct sun from windows
Radio antennas are in the center of the room for least interference, I can go on
Wiring in the ceiling is way easier than down a wall.
What if the wall needs to move, then what?
What if there is no wall. Just cubicles the Hub is ideal
Vandalism is far less a concern compared to switches or stats on the wall.

## Slide 42: O3 System - Components
Room Control App

## Slide 44
Room Location Hubs know when you’re nearby
Easy
Experience Activity Control Hub feedback – LED ring, sound
Room Control App
Notes: Just a quick note on the Room Control App,
It senses which room you’re in and gives you control over elements in that room.
Highly integrated, highly occupant centric, highly convenient.

## Slide 45: O3 System - Components
enteliWEB

## Slide 47
IIS Web Server
Clients (Web Browsers)
Web Services (REST)
PHP
(Core Logic)
PHTML
(Templates)
BIRT Runner
(Reports)
Historian Database
Local MySQL Database
eWEB Connect Service
BACnet Server 4.0
Delta PHP Extension
BACnet Site A
BACnet Site B
BACnet Site C
BACnet Site D
http/https
Real-Time-Analytics
Real-Time Applications
ODBC
Trendlog
Events, Alarm^s
Delta provides a full suite of Building Automation System components
Use Web Services, or use the ODBC connector